## Slide 1: RFID BASED SMART ATTENDENCE SYSTEM
Presented by:
SHASHIKANT DWIVEDI (2025041245)
SUBHASH SINGH (2025041251)
NIKHIL KUMAR (2025041261)
SARANG GOPALAN (2025041265)
SATYAM PRAJAPATI (2025041260)
B.Tech (ECE) Project Presentation
Department of Electronics and Communication Engineering,
Madan Mohan Malaviya University of Technology, Gorakhpur (UP) , India

## Slide 2: Outline of Presentation
Introduction & Motivation
Block Diagram & Circuit
Technologies Used
Uniqueness & Innovation
Impact, Feasibility & Conclusion
References & Q&A

## Slide 3: Project Description/Objective/Motivation
The Problem
Traditional roll-call is time-consuming and prone to proxy attendance
Paper registers are error-prone and lack real-time accessibility
No centralised tracking for faculty or administration
Our Objective
Automate attendance using RFID and ESP32 microcontroller
Transmit records wirelessly via WiFi to a cloud database
Display live attendance on a responsive web dashboard
Save time, improve accuracy, and enhance transparency

## Slide 4: Block Diagram and Circuit Description
• The RFID card is scanned using the RC522 reader. • The reader sends the UID to the ESP32 via SPI communication. • ESP32 processes the data and sends it to the server using WiFi. • The server stores the attendance in the database. • The web dashboard displays attendance for students and faculty.
• The RC522 RFID module is connected to ESP32 using SPI interface. • Pins used: SDA, SCK, MOSI, MISO, RST, 3.3V, and GND. • ESP32 provides power and controls communication with the RFID module. • When a card is scanned, RC522 sends data to ESP32 for processing.

## Slide 5: Technology and Components Used
ESP32 Microcontroller
Dual-core MCU with built-in WiFi and Bluetooth; handles UID processing and cloud communication
RFID RC522 Module
13.56 MHz MIFARE reader; communicates with ESP32 via SPI interface at low power
Firebase Realtime DB
Google's NoSQL cloud database; stores attendance records and enables live sync to the dashboard
Web Dashboard
Built with HTML, CSS, and JavaScript; separate panels for students and faculty with live data
WiFi Communication
ESP32 connects to local network; data pushed to Firebase over HTTPS in near real time
Low-Cost BOM
Total hardware cost ~₹800–1,200: ESP32 (₹400), RC522 (₹150), Cards (₹30 each), misc. components

## Slide 6: Differentiation/Uniqueness/Innovation of Project

## Slide 7: Impact and Feasibility of Product
RFID SYSTEM
TIME SAVING
ACCURACY
REDUCE PROXY
BETTER MANAGEMENT
IMPACT
• Saves time and reduces manual effort • Improves accuracy • Reduces proxy attendance • Real-time tracking • Useful for institutions
FEASIBILITY
• Low-cost implementation • Easy setup and maintenance • Scalable system • Uses existing WiFi • Practical for real use

## Slide 8: Conclusion and Future Scope
Automated
Accurate
Time Saving
Real -Time
Efficient Attendence System
Reliable and Scaleble
RFID SYSTEM
MOBILE APP
FACE RECOGNITION
QR ATTENDENCE

## Slide 9: Upcoming Plan/Layout
🔷 Role of Team Members
• Hardware Development: ESP32 and RC522 interfacing • Web Development: Dashboard design (Student & Faculty portal) • Backend & Database: Attendance storage and API handling • Testing & Integration: System testing and debugging
🔷 Project Timeline / Approach
• Phase 1: Hardware setup and RFID integration • Phase 2: Web application development • Phase 3: Database connection and real-time data transfer • Phase 4: Testing, debugging, and final deployment
🔷 Progress Achieved Till Now
• Successfully connected ESP32 with RC522 module • RFID card reading and UID detection completed • Web dashboard for attendance tracking developed • Real-time data transfer implemented

## Slide 10: References (Sample to write proper references)
Espressif Systems. ESP32 Technical Reference Manual. Espressif Systems, 2023. Available: https://www.espressif.com/en/support/documents/technical-documents
NXP Semiconductors. MFRC522 Standard Performance MIFARE and NTAG Frontend, Rev. 3.9. NXP, 2016. Available: https://www.nxp.com/docs/en/data-sheet/MFRC522.pdf
Google LLC. Firebase Realtime Database Documentation. Google Developers, 2024. Available: https://firebase.google.com/docs/database
K. Ashton, "That 'Internet of Things' Thing," RFID Journal, vol. 22, no. 7, pp. 97–114, 2009.
S. Sharma and A. Gupta, "IoT-Based Attendance Management System Using RFID and Cloud," Int. Journal of Engineering Research & Technology (IJERT), vol. 9, no. 6, 2020.
R. Patel et al., "Design and Implementation of RFID-Based Attendance System with Real-Time Database," Proc. IEEE ICCUBEA, Pune, 2021, pp. 1–5.

## Slide 11
THANK YOU